## Slide 1
Wi-Fi Management and Security
L2 Network
|
|
|
|
|

## Slide 2: Module 1
Module 1 will be covering the following topics:
  Introduction to Wi-Fi Networks
      802.11 Standards Family
      Building blocks of Wi-Fi technology (Spectrum Reuse, Carrier Sensing, Modulation, Bandwidth Aggregation, MIMO, Roaming, QoS, VoWiFi)
      802.11ax Overview
  End-to-End Wi-Fi Network Architecture
      Core Network ( AAA, Captive portal, WAG)
      Wireless Authentication Models and Mechanisms
      Enterprise, Public
  WIPS and WIDS

## Slide 3: Session 1
Spectrum
Bands
NTA / FCC
802.11

## Slide 4: Spectrum

## Slide 5: Spectrum

## Slide 6: Bands
Band Name | Abbreviation | Frequency and wavelength | Examples
Tremendously low frequency | TLF | <3Hz ¦ 100,000 Km | -
Extremely Low Frequency | ELF | 3–30 Hz ¦ 100,000–10,000 km | Communication and submarines
Super Low Frequency | SLF | 30–300 Hz ¦ 10,000–1,000 km | Communication and submarines
Ultra Low Frequency | ULF | 300–3,000 Hz ¦ 1,000–100 km | Communication with submarines, landline telephony, fax machines
Very Low Frequency | VLF | 3–30 kHz ¦ 100–10 km | Navigation, time signals, communication with submarines, wireless heart rate monitors
Low Frequency | LF | 30–300 kHz ¦ 10–1 km | Navigation, time signals, AM longwave broadcasting
Medium Frequency | MF | 300–3,000 kHz ¦ 1,000–100 m | magnetic resonance imaging, positron emission tomography wireless telegraphy,
High Frequency | HF | 3–30 MHz ¦ 100–10 m | Citizens band radio, aviation communications, marine and mobile radio telephony, magnetic resonance imaging, positron emission tomography.
Very High Frequency | VHF | 30-300 MHz ¦ 10-1 m | FM broadcasts, radars, line-of-sight ground-to-aircraft and aircraft-to-aircraft communications, radioteletype, maritime mobile communications, weather radio, magnetic resonance imaging, positron emission tomography
Ultra High Frequency | UHF | 300–3,000 MHz ¦ 100–10 cm | Cable television broadcasting, radars, microwave devices/communications, radio astronomy, mobile phones, wireless LAN, Bluetooth, ZigBee, GPS satellite radio cordless phones, internet, satellite broadcasting, weather satellites, satellite phones
Super High Frequency | SHP | 3–30 GHz ¦ 10–1 cm | Microwave devices/communications, communications satellites, cable and satellite television broadcasting, satellite broadcasting, communication satellites, weather satellites cordless phones,
Extremely High Frequency | EHF | 30–300 GHz ¦ 10–1 mm | Satellite broadcasting, communication satellites, weather satellites, directed-energy weapon, Wireless Lan 802.11ad.
Terahertz or tremendously high frequency | THF | 300–3,000 GHz ¦ 1–0.1 mm | Experimental medical imaging to replace X-rays

## Slide 7: Allocation and Regulation of Radio Spectrum
Nepal Telecommunication Authority
Federal Communications Commission (FCC)
Ofcom
International Telecommunication Union (ITU)

## Slide 8: IEEE
IEEE (Institute of Electrical and Electronics Engineers) was formed on January 1, 1963.
Merger of two organizations: the American Institute of Electrical Engineers (AIEE), founded in 1884, and the Institute of Radio Engineers (IRE), founded in 1912.
IEEE (Institute of Electrical and Electronics Engineers) is the world's largest technical professional organization dedicated to advancing technology for the benefit of humanity.

## Slide 9: IEEE 802 Standards
  IEEE 802 sets of LAN technical standards.
  Standard developed and maintained by IEEE 802 LAN/MAN Standards Committee, started on 1979.
  Some of the Standards:
  IEEE 802.1
  IEEE 802.3
  IEEE 802.11
  IEEE 802.15
  IEEE 802.16
  IEEE 802.22

## Slide 10: Session 2 Introduction to Wi-Fi Networks 802.11
  802.11 standards is defined through specification of WLAN
    *An over-the-air interface between wireless clients and base station, accepted by IEEE in 1997.

## Slide 11: 802.11 Standards Family
IEEE 802.11 – 1997
IEEE 802.11b (Wi-Fi 1)
IEEE 802.11a (Wi-Fi 2)
IEEE 802.11g (Wi-Fi 3)
IEEE 802.11e – 2005
IEEE 802.11n (Wireless-N or Wi-Fi 4)
IEEE 802.11ac (Gigabit Wi-Fi or Wi-Fi 5)
IEEE 802.11 ad (WiGig)
IEEE 802.11 ah (Wi-Fi HaLow)
IEEE 802.11ax (Wi-Fi 6)

## Slide 12
IEEE 802.11 Standards | Band | Introduced | Speed
IEEE 802.11 1997 | 2.4 GHz | 1997 | 1 Mbps to 2 Mbps
IEEE 802.11a (Wi-Fi 2) | 5 GHz | 1999 (OFDM) | 54 Mbps
IEEE 802.11b (Wi-Fi 1) | 2.4 GHz | 1999 (DSSS) | 11 Mbps
IEEE 802.11g (Wi-Fi 3) | 2.4 GHz | 2003 (Backward Compatibility) | 54 Mbps
IEEE 802.11e 2005 | 2.4 and 5 GHz | 2007 (WMM-QoS) | 54 Mbps
IEEE 802.11n (Wireless-N or Wi-Fi 4) | 2.4 or 5 GHz | 2009 (MIMO) | 600 Mbps
IEEE 802.11ac (Gigabit Wi-Fi or Wi-Fi 5) | 2.4 and 5 GHz | 2013 (Dual Band / MU-MIMO) | 450 Mbps / 1300 Mbps
IEEE 802.11 ad (WiGig) | 60 GHz | 2012 (60 GHZ) | 6.7 Gbps
IEEE 802.11 ah (Wi-Fi HaLow) | 900 MHz | 2017 (900 MHz / Extended Range) | 347 Mbps
IEEE 802.11ax (Wi-Fi 6) and Extended | 2.4 and 5 GHz / 6GHz only (WiFi6E) | 2019 (OFDMA, MU-MIMO, 1024-QAM) | 10 Gbps

## Slide 14: Building blocks of Wi-Fi technology
Spectrum Reuse
Carrier Sensing
Modulation
Bandwidth Aggregation
MIMO
Roaming
QoS
VoWiFi

## Slide 15
Spectrum Reuse: Selecting and allocating channels groups for all of the stations within a system.

## Slide 16
Carrier Sensing: Mechanism used in wireless communication systems
Clear Channel Assessment (CCA): (ED) / (CSMA/CA)

## Slide 17
Modulation: Modulation is what wireless networks use to send data.

## Slide 18
Bandwidth Aggregation: Spreading communications traffic over more than one channel between two devices to increase total bandwidth.

## Slide 19
MIMO: Antenna systems used in modern wireless standards, to sends the same data as several signals simultaneously through multiple antennas, while still utilizing a single radio channel.

## Slide 20
Roaming: Standards designed to make it easier for users to move from one wireless access point to another without losing their connection.

## Slide 21
QoS: WMM, which enhances QoS by prioritizing data packets according to different categories.

## Slide 22
VoWiFi: Process of using Wi-Fi over cellular data, for voice calling for supported device.

## Slide 23: 802.11ax Overview
Introduced in 2019, as 802.11ax “Wi-Fi”
  2.4GHz and 5GHz
  Theoretical speed up to 10 Gbps.
  Compatible with 802.11a/b/g/n/ac.
  Supports Technologies as:
    OFDMA, MU-MIMO, 1024-QAM and more
Later introduced Wi-Fi 6E”Extended” in early 2021
  2.4GHz / 5GHz and 6GHz
  less congested frequency bands.

## Slide 24: Session 2 End-to-End Wi-Fi Network Architecture
Core Network (AAA, Captive portal, WAG) *Authentication, authorization, and accounting (AAA)

## Slide 25: Captive portal
Web page that the user of a public-access network is obliged to view and interact with before access is granted

## Slide 26: WAG (Wi-Fi Access Gateway)
An element in a network that serves to route data packets from a wireless LAN to another network.
Viewed as a combination of Wi-Fi controller, router, DHCP server, and firewall.

## Slide 27: Wireless Authentication Models and Mechanisms
Wireless Authentication: *Open authentication *Shared authentication *Extensible Authentication Protocol (EAP)
Wireless Encryption: *Wired Equivalent Privacy (WEP) *Wi-Fi Protected Access (WPA) *Wi-Fi Protected Access 2 (WPA2)

## Slide 28
Wireless Authentication: *Open authentication: Simplest of the method, only require end device to be aware of the SSID ”Service-Set Identifier” *Shared authentication: Commonly used method on individual and small business WLAN Implementation. Using a Shared Key”PSK” at each end. *Extensible Authentication Protocol (EAP) Method used by Enterprises, utilizing authentication server for authentication using variety of credential options.

## Slide 29
Wireless Encryption: *Wired Equivalent Privacy (WEP) Utilizes RC4 “Rivest Cipher 4” *Wi-Fi Protected Access (WPA) Utilizes the TKIP“Temporal Key Integrity Protocol” *Wi-Fi Protected Access 2 (WPA2) Utilizes AES “Advanced Encryption Standard”

## Slide 30: Enterprise

## Slide 31: Public

## Slide 32: WIPS and WIDS
WIDS, a system of sensors is used to monitor the network for the intrusion of unauthorized devices, such as rogue access points.
WIPS, the system not only detects unauthorized devices, but also takes steps to mitigate the threat by containing the device and detaching it from the wireless network.
Threats *Rogue APSs *Soft Rogue Aps.

## Slide 33: END of Module 1
Thank You