## Slide 1
Wi-Fi Management and Security
L2 Network
|
|
|
|
|

## Slide 2: Module 2
Module 2 will be covering the following topics: How to Find the Best Wi-Fi ONU router Placement?
  Guidelines for Finding the Best Placement for a Wi-Fi ONU router:
  1. Make Your ONU the Center of Attention
  2. Get Your ONU Off the Floor
  3. Avoid Physical Obstacles
  4. Be on the Lookout for Interference
  5. Reposition Your ONU’s Antennas
  6. Bonus: Update Your ONU.
What are Some Other Ways to Boost Wi-Fi?
  Check Your Wi-Fi Signal Strength.

## Slide 3: How to Find the Best Wi-Fi ONU Router Placement?
Take into consideration
  Physical obstacles
  Layout of the area
  Look for potential interference in the spectrum.

## Slide 4: Guidelines for Finding the Best Placement
Make Your Router the Center of Attention.
  *Move it to Central Location.
Example 1

## Slide 5
Example 2
1. Make Your Router the Center of Attention
Always find the Center Point of the area layout

## Slide 6
1. Make Your Router the Center of Attention
Example 3

## Slide 7
Example 1
2. Get Your ONU Router Off the Floor
Do not setup router on the base of the House

## Slide 8
Example 2
2. Get Your ONU Router Off the Floor
Do not setup router on the base of the House

## Slide 9: 3. Avoid Physical Obstacles
Such as cabinets and large appliances.
Reflective surfaces can bounce off Wi-Fi signals,
  Will cause performance issues.

## Slide 10
Do not put the router in a cabinet
Keep the router out in the open
Example 1
3. Avoid Physical Obstacles

## Slide 11
Example 2
3. Avoid Physical Obstacles

## Slide 12
Find the Best place and Keep the router out in the open
3. Avoid Physical Obstacles
Example 3

## Slide 13
3. Avoid Physical Obstacles
Example 4
Bathrooms/Kitchens are not recommended areas to place routers.

## Slide 14
3. Avoid Physical Obstacles
Example 5
Go through the surrounding objects and avoid the obstacles

## Slide 15: 4. Be on the Lookout for Interference
Channel Overlap
Avoid devices like,
  Microwave ovens
  Monitors
  Wireless security cameras
  Cordless phones
  and various smart home devices

## Slide 16
4. Be on the Lookout for Interference
Keep the router away from other electronics
Example 1

## Slide 17
Do Not Place router close other smart electronics Devices.
Example 2
4. Be on the Lookout for Interference

## Slide 18: 5. Reposition Your Router’s Antennas
Router with adjustable antennas, experiment with their position to improve the quality of your Wi-Fi signal.
Reposition antennas and experiment with their position to improve Signal.

## Slide 19
5. Reposition Your Router’s Antennas
Example 1
How the signal is being distributed

## Slide 20: 6. Bonus: Update Your ONU / Router
    Check for updates and Install available updates.

## Slide 21
Do not provision ONT with disabled option for every Nokia ONT.
6. Bonus: Update Your ONU
Example

## Slide 22: What are Some Other Ways to Boost Wi-Fi?
Improve your Wi-Fi security settings.
Control bandwidth-hungry applications.
Upgrade your Wi-Fi network.

## Slide 23: Upgrade your Wi-Fi network
Wi-Fi Booster

## Slide 24: Upgrade your Wi-Fi network
Mesh Router “Nokia Beacon, Google Wi-Fi, TP-link Deco Mesh”

## Slide 25: Check Your Wi-Fi Signal Strength
Check Wi-Fi signal strength using several analyzer tools “Netspot, Inssider, etc”.
Example 1 Tool: Netspot

## Slide 26
Verify SSID
Verify your RSSI
Check your Wi-Fi channel and prevent channels overlap
Check Your Wi-Fi Signal Strength
Example 2 Tool: Netspot

## Slide 27
<< Check for overlapping channels
<< Verify RSSI strength
Example 3
Use Wi-Fi Analyzer Tool

## Slide 28: End of Module 2
Thank You

## Slide 29: Module 3
Module 3 will be covering the following topics:
    Configuration and Troubleshooting
      Wireless configuration
      Wi-Fi Troubleshooting “Better Performance”
    Introduction to Mesh Wi-Fi Router “Nokia Beacon”
      Nokia Recommended Placement
      Beacon Installation

## Slide 30: Configuration and Troubleshooting
Nokia Wi-Fi ONU ”2.4GHz”
Wireless Interface enable/disable
802.11 Standard
Channel Range
Wi-Fi Channel for transmission
Antenna Power
Wireless Multimedia for QoS
Client Limit

## Slide 31: Nokia Wi-Fi ONU
Support Multiple SSID
“Service Set Identifier”
Network Name
Enable Selected Network Name
Show Wi-Fi Name
Wireless interface mode Route / Bridge
Wireless Client Isolation “Useful for ”
Client Limit for selected network
Wireless Encryption
Wireless Encryption method according to selected version
Key for authentication
Wi-Fi Protected Setup
Routing Domain

## Slide 32: Nokia Wi-Fi ONU
Wireless Interface enable/disable
Channel Range
Antenna Power
Wi-Fi Channel for transmission
Wireless Multimedia for QoS
MIMU technology
Client Limit
Nokia Wi-Fi ONU ”5 GHz”

## Slide 33: Nokia Wi-Fi ONU
“Service Set Identifier”
Support Multiple SSID
Network Name
Enable Selected Network Name
Show Wi-Fi Name
Wireless interface mode Route / Bridge
Wireless Client Isolation “Useful for Open / Guest Network ”
Client Limit for selected network
Wireless Encryption method according to selected version
Key for authentication
Wi-Fi Protected Setup
Routing Domain

## Slide 34: Wi-Fi Performance
Lookout for overlapping channels.
Verify the signal status of the other transmitting channels.

## Slide 35: Wi-Fi Performance
Basic Service Set Identifier
Service Set Identifier
Radio Signal Strength Indicator
Frequency Band
Transmitting channel
Channel width
Encryption Method
Standard

## Slide 36: Wi-Fi Performance
Look for unexpected users

## Slide 37: Wi-Fi Performance
Verify active devices and its signal strength.

## Slide 38: Wi-Fi Performance
Enable required Technologies and Features.
  Use of channel width
  WMM
  MIMO
  Standards

## Slide 39
Introduction to Mesh Router Wi-Fi “Nokia Beacon”
Easy Plug and Play setup and implementation.
User friendly mobile app to play on mesh features.
Efficient channel and signal optimization.
Intelligent mesh routing.
Fast reconnection to AP.
Seamless Wi-Fi connection.
Reduced Wi-Fi interference.
Seamless Roaming feature.
Reduced Wi-Fi Dead Zones.

## Slide 40: Nokia Recommended Placement
Using Phone to find suitable location.

## Slide 41: Nokia Recommended Placement
Network Map & Speed test to verify.

## Slide 42: Beacon Installation
PnP Installation
*Step 1: Desktop Mounting with Simple PnP setup.
*Step 2: Power ON and connect WAN Ethernet to ONU/Modem until LED is blue. This setups first beacon as Root device.
*Step 3: First Beacon will act as Root. Once you set as root and associate with account its all set in Nokia Wi-Fi Cloud. *Step 4: Connect another beacon to first beacon via Ethernet same as step 2. This sets wireless mesh after Ethernet is disconnected.
Note : Changing Root later will require factory default setting or de-association with account from Nokia Wi-Fi Cloud via Nokia help Center in app.
Phone App : Nokia Wi-Fi
*Step 1: Use the App to scan the QR code at the bottom of Beacon.
*Step 2: Sign up to see the user friendly setup.

## Slide 43: Beacon Installation
Installation from Beacon itself (login to page : 192.168.18.1)

## Slide 44
End of Module 3 Thank You !